## Slide 1: HACKING THE USB WORLD
ENUMERATION AND THE CONTROL ENDPOINT
WITH FACEDANCER
KATE TEMKIN & DOMINIC SPILL

## Slide 2
ENUMERATION
enumeration allows devices to be identified and paired with the correct drivers automatically

## Slide 3
to support enumeration, every USB device must support a standard protocol on EP0
this protocol involves our first formal type of transfer: usb control requests

## Slide 4
each control transfer is made up of a number of transactions…
…which form a simple command-and-response protocol.

## Slide 5
It’s often helpful to think of these transactions at a higher level of abstraction…

## Slide 6
Each control transfer begins with a setup stage describing the transactions to be performed.
SETUP STAGE

## Slide 7
If a device doesn’t support a given request,
it can STALL the setup stage by issuing a STALL handshake instead of an ACK.
SETUP STAGE

## Slide 8
If the request has a non-zero length, the transfer has a data stage compromised of one or more IN or OUT data transactions.
DATA STAGE
If the device isn’t ready for the data stage, it can NAK to buy time to become ready.
The data stage ends when a short packet is received– that is, a packet less than the maximum packet size. (i.e. 8 bytes for LS, 64 bytes for FS)

## Slide 9
Each control transfer ends with a status stage, which confirms both sides agree that a transaction completed correctly.
STATUS STAGE
The status stage is always in the direction opposite the last transaction, to ensure both sides have a chance to ACK.

## Slide 10
CONTROL REQUESTS
The setup stage of a control transfer describes the type of request, the size and direction of the request’s data stage, and provides arguments.
The USB specification requires all devices to support a number of standard control requests, which are used for enumeration and configuration.

## Slide 11
SET_ADDRESS REQUESTS
Every device starts with an address of zero.
A set-address request is one of the first requests commonly issued to a device, and assigns it an address for future communications.
This request has a length of zero, and thus no data stage. It communicates only via setup arguments:
value = address to be assigned

## Slide 12
GET_DESCRIPTOR REQUESTS
A primary goal in enumeration is to allow USB devices to self-describe. Accordingly, devices can provide summaries of themselves and their functions called descriptors.
There are a multitude of descriptors a device can provide. Some examples:
device descriptors provide a high-level overview of the device
string descriptors contain strings that are referenced elsewhere

## Slide 13
DEVICE DESCRIPTORS
The device descriptor provides everything a host needs to get an idea of who the device is:
Vendor ID
Product ID
Device ‘class’ in formation
References to string names.
Max size of packets on the control endpoint.